## Slide 1: HbbTV -Quick Glance
by
Shunmuga Sundaram Ponniah

## Slide 2: HbbTV
Hybrid Broadcast Broadband Television
Pan European Standard
Specifications will approved by ETSI
Application may be launched from either Broadcast Signalling or XAIT(manual) Signalling
Data may be comes from either Carousel or Internet
Covered basic FTA functionality and extensions like 7-days EPG, PVR, DRM, CA etc..

## Slide 3: HbbTV
Application authoring is easier than MHP, MHEG5 or other interactive applications
Having an essential knowledge in HTML/JS for application development
CE-HTML is an additional standard used for consumer electronics application
Browser is a sand-box environment so applications are more safe to run

## Slide 4: HbbTV
DRM playback also supported
Application can control/access the DVB functionality over OIPF extensions
Startup applications are known as Red-Button apps
Digital Text are more interactive than Traditional/Standard Teletext application

## Slide 5: Where it is

## Slide 6: How it works
WebServer
Broadcast
Headend
Hybrid STB
Return Channel
AV Content

## Slide 7: HbbTV/1.0
Playback of broadcast and IP-streamed media
Download media to persistent local storage
Access to channel list and now/next EPG data
Broadcast-related and broadcast-independent applications

## Slide 8: HbbTV/1.5
EIT-Schedule access
MPEG DASH
DRM APIs (No specific DRM solution mandated by HbbTV, but one may be mandated for specific markets by trademark license holders)

## Slide 9: HbbTV/2.0
Improved support for HTML5.
Companion screen app launching and synchronization.
Push VOD support.
Improved support for ad insertion.
Improved synchronization between media and applications.
Support for HEVC video.
Improved support for MPEG DASH.

## Slide 10: Specifications
OIPF
HbbTV
OIPF-T1-R2-Specification-Volume-5-Declarative-Application-Environment-v2_3-2014-01-24.pdf
ts_102796v010201p.pdf
ts_102809v010101p.pdf
DVB
W3C
CEA-2014 revision A
#
[references]

## Slide 11: System Overview
Operating System
HAL
Middleware
HbbTV Apps
MHEG5 Apps
Terminal Apps
Connected TV Apps
Browser
HbbTV
Application
Manager
OIPF
Plugin
Application Layer

## Slide 12: How RedButton starts
T
Receiving the Signal
Collect the AIT
Section and Parse
the descriptors
Organize the App
by ControlCode &
priority wise
If ControlCode is
AUTOSTART, load
the relevant URL
Collection the
Application resource
Accessing the
DVB components
URL Sharing
Accessing through OIPF Extension
Resource
Collection
Passing
AIT Info
AIT Collector/ Parser
Application Manager
Browser
DSMCC / IP
Middleware Components
Broadcast Signal

## Slide 13: Thank You !!!
Please write your suggestions or queries to
ssundaramp@outlook.com